## Slide 1
Don Williams - Image Science Associates - d.williams@imagescienceassociates.com
Measuring and Monitoring
Cultural Heritage Digital Image Quality

## Slide 2
Why makes cultural heritage
imaging different ?
Future Re-purposing
  Variety of use cases
  Information durability
Information critical
  Images, not pictures
Scientific and
research component
High volume, High speed
  Think manufacturing
  Think error management

## Slide 3: What you’ll see
Background
  Space + Light = Image
  Image Digitization
Digitization hardware components
Vocabulary
Performance Metrics - Signal & Noise
  Tone, White Balance, Color
  Resolution
  Noise
  Artifacts
Workflow Monitoring
Test plans

## Slide 4: What is an image ?
A Spatial Map of Energy*
for our purpose
A two dimensional mapping of light energy ( red, green, blue, lightness)
Space and Light
* Applies to 3D, UV, IR, other colors too

## Slide 5
What is Digitization?
Conversion (capture) of analog information in any form (text, photos, voice, etc.) to a digitally encoded form. This encoded information can be easily processed, stored, and transmitted through circuits, equipment and networks.
The encoded information can then be decoded into a surrogate analog form. (display)

## Slide 6
What is a Digitized Image ? - general imaging steps -
Digitize
raw
Interpret &
Render
Object
Display
Or
Print
CAPTURE
Encode - Converting light to numbers
DISPLAY
Decode - Converting numbers to light
“The Digital Image”
An encoded proxy image
Digitize
Processed

## Slide 7
Why Visual Assessments
of Color and Tone can be unreliable

## Slide 8
What is a Digital Imaging System? ( for capture)
The performance of a digital capture system at the sensor and beyond is influenced by all of the above in addition to operator training and environment.
The different ways an image is modified at capture
Digital image file
light
source
Image
forming
optics
sensor
sample
Processing

## Slide 9
Digital Imaging Science -101
Light hits object
Object responds
Response is delivered
Delivery is digitized
What has changed ?

## Slide 10
Digital Imaging Science -101
Light hits object
Object responds
Response is delivered
Delivery is digitized
What has changed ?

## Slide 11: How is the Reflectance / Transmission of Objects Characterized ?
Density = - log10 (reflectance)
Like the Richter Scale for measuring earthquake magnitude, density is also a “log” based metric. Each unit change in density is a 10x change in the magnitude of light ( reflectance). Log based units are frequently used for gauging equal differences in perceived magnitude.
Incident
Illumination -
1000 units
1000 units reflected
1000 units incident
= 1.000 reflectance
= 0.0 density
Reflective
or
transmissive
hardcopy
100 units reflected
1000 units incident
= 0.100 reflectance
= 1.0 density
10 units reflected
1000 units incident
= 0.010 reflectance
= 2.0 density
1 units reflected
1000 units incident
= 0.001 reflectance
= 3.0 density

## Slide 12
Digital Imaging Science -101
Light hits object
Object responds
Response is delivered
Delivery is digitized
What has changed ?

## Slide 13: Know your Collection - Typical density ranges ( think light ) for collection content -
B&W Photographic Paper
B&W Photographic Film
Kodachrome film
Color photographic paper
Q-13 target
Munsell papers
Motion picture print film
Non Photographic reflective material
Density

## Slide 14
Digital Imaging Science -101
Light hits object
Object responds
Response is delivered
Delivery is digitized
What has changed ?

## Slide 15: The Lens
The most important item affecting resolution in a camera
http://www.cambridgeincolour.com/tutorials/camera-lenses.htm
Aperture (F-number) extremes tend to produce the worse results
Higher F-numbers increase depth of focus but resolution suffers
Lower F-numbers tend to perform better but suffer from artifacts
Always inspect for color misregistration at corners of the field of view
Some lenses (telecentric design) are optimized for digital cameras
Zoom lenses are convenient but suffer from design compromises.

## Slide 16
Color MisRegistration - color focus shift-

## Slide 17: Types of Digital Capture Systems - Scanners vs. Cameras -
Fully Integrated – all capture components combined into a single plug-and-play scanner unit
  Flatbed scanners – Epson ($), Creo IQSmart3 ($$$)
  Copy Stand – Zeutschel, I2S products,
  Special Purpose - Kirtas, Treventus, and Qidenus
D-I-Y Copy stands ( i.e. camera-on-a-stick)
  Camera Backs – Betterlight, Hasselblad, Sinar, Phase One
  Digital SLRs – Canon EOS, Nikon

## Slide 18: Sensor / Detector Technologies
What is the least expensive way to quickly capture
large amounts of high quality color image information ?
( cost ,speed, volume, quality)
Single detector or one detector for each color – flying spot scanners, drum scanners.
Linear arrays – one dimensional ordered arrangement of single detectors
Area arrays – two dimensional ordered arrangement of single detectors.
Step and Repeat (Macro or Micro) area strategy – capture and combine several area captures into a single large image

## Slide 19: 2-D Area Arrays - Color Filter Array (CFA) pattern -
From : The Focal encyclopedia of photography
Three filter mosaic pattern ( Red, Green, Blue) of sensors. Sometimes other patterns are used but the “Bayer” pattern ( shown here) is by far the most popular. Used in virtually all consumer and professional digital cameras
One shot /one layer, sparsely populated color capture. Fully populated color achieved by interpolation algorithms (de-mosaicing) or micro-stepping.
Color filters integrated onto the sensor chip at manufacturing.
Occasionally will have subtle checkerboard artifacts or color aliasing rainbows in final delivered image.

## Slide 20
Rainbow artifacts from CFA reconstruction
Usually occurs with fine spaced repetitive patterns
- fabrics, engravings, halftones, target features -
Due to the inability of the processing algorithm to
accurately estimate the missing color pixels of a CFA

## Slide 21: Linear Arrays ( Tri-linear)
From : The Focal encyclopedia of photography
Three filtered ( Red, Green, Blue) rows of sensors
The sensor stares at the object in the row dimension and scans by the object in other direction. Sometimes called a pushbroom.
Used in scan back cameras and sheet fed scanners. ( e.g. BetterLight, PhaseOne FX,), flatbed scanners and most film scanners.
Frequently have different performance behaviors in the two different directions.
Frequent streaking artifacts

## Slide 22
Digital Imaging Science -101
Light hits object
Object responds
Response is delivered
Delivery is digitized
What has changed ?

## Slide 23: Then a miracle occurs !
Bit Depth - Light intensities reaching the detector are assigned one of 2N digital count values for each of M color channels. For high quality re-purposeable images N= 14-16 bits and M=3 color (RGB) channels. This is referred to as N bit quantization.
28 = 256 values ( 0-255) : 216 = 65536 values (0-65535)


Light  electricity  numbers

## Slide 24
21 = 2 levels ( 0-1 ) one bit or bi-tonal image
28 = 256 levels ( 0-255 ) 8 bit or grayscale image
2 (8*3) = 256 levels for each of three colors. True or 24 bit color.
Raw or Safety Master image files are often delivered as 16 bit/channel or a total of 48 bit color. These files are often maintained as digital or safety masters because they allow maximum future utility.
2(16*3) = 65536 levels for each of three colors. 48 bit color
More commonly, a scanner’s or camera’s software will use the higher number of bits to provide a “delivered file” of lesser number of bits that is consistent with a user’s specific application. Future utility of this finished file is compromised though.
N bits – M Channels

## Slide 25: Image Processing - the brains -
Image processing functions will affect imaging performance measurements. These include,
  Image resizing, rotation
  Sharpening
  Tone/Color adjustments
  Color profile changes
  Noise reduction
Two approaches for performance measurement
  Practice - measure the “as delivered” image file consistent with workflow practices.
  Benchmarking – measure the raw image file with as many functions as possible disabled.

## Slide 26
Digital Imaging Science -101
Light hits object
Object responds
Response is delivered
Delivery is digitized
What has changed ?

## Slide 27: -Targets - a requirement for disposable dog biscuit packaging

## Slide 28
Targets as Jewelry ?

## Slide 29: Targets - Health checks for detecting imaging ills- - Act as ground truth for before / after evaluation -
light
source
Image
forming
optics
sensor
sample
User Interface & Processing
Digital image file
Targets and Performance
Analysis Software

## Slide 30: How metrics are used to measure performance ?
Accuracy - Image values from a target are compared with established aim values. These values are typically use-case dependent.
Precision - Tolerances around these aims are also provided. Small tolerances imply greater precision but also higher production costs. The opposite is true for large tolerances.
Consistent performance is often more important than accuracy.
variation
bias
Aim – The point or set of points intended to be hit

## Slide 31
Capability
Behavior under optimal conditions
Performance
Behavior in actual use
Capability vs. Performance

## Slide 32
FADGI provides quantitative guidelines on accuracy and precision levels for creating a durable, re-purposeable digital image object
Use case dependent
ISO based metrics
precision rating
Measures of goodness
10 years of learning
Where FADGI fits in

## Slide 33
Why you should care
Quality control and industry compliance
Consistent product
Managing expectations – acceptance testing
Accurate Metadata population
Diagnostics – problem solving and image processing identification. Less rework.
Effective communication

## Slide 34
Image Speak - Vocabulary
- staying dry in a storm of performance idioms -
Resolution
Exposure
Sharpening
Delta E
White
Balance
Dynamic
Range
Gamma
Exposure
Depth of
field
Flare
Shading
Noise
Geometric Distortion
Wobble
Aliasing
Signal
Noise
Lateral Color
Error
Sharpness
Acutance

## Slide 35: Imaging Performance Framework How terminology and metrics are organized
Foundation Metrics | Primary Metrics | Derivative Metrics
Signal | Tone Transfer Function Opto-Electronic Conversion Function (Large Area Signal ) | Tone / Exposure
 |  | White Balance
 |  | Gamma
 |  | Color / Delta E
 | Spatial Frequency Response (Small Area Signal ) | Resolution
 |  | Sharpening
 |  | Sampling Efficiency
Noise | Light Intensity Distortions | Random / White Noise
 |  | Banding / Streaking
 |  | Vignetting / Shading
 |  | Defects
 | Geometric Distortions Artifacts | Chromatic Aberration
 |  | Pincushion / Barrel
 |  | Aliasing / Moire

## Slide 36
Device Target Elements
ISO Frequency Response (SFR) and resolution over the field of view. (7” x 10”)
Human interpretable resolution features
Dimensional scales for to confirm “dpi” levels
Automated feature detection
Neutral gray uniform background
Self described colorimetric patch annotations
Ten spectrally neutral gray patches

## Slide 37
Object Target Elements
• Concise version of the device target.
• Enables 100% quality control.
• Calibrated spatial & colorimetric ground truth
to original object ( Think sustainability )
• Same features as device target
- SFR and Resolution
- Spectrally neutral grayscales
- Dimensional scales
- Automated feature detection
- Self described colorimetry

## Slide 38: Graphical Representation of OECF
Density
OECF example
0
50
100
150
200
250
0
0.5
1
1.5
2
neutral (gray) density
average green count value ( 8 bit)

## Slide 39
Tone transfer aim comparisons

## Slide 40
Gamma 2.2 aim
PShop Brightness adjustment effect on OECF
Over-exposed
Under-exposed

## Slide 41
Gamma 2.2 aim
PShop contrast adjustment effect on OECF
Over-exposed ?
Under-exposed ?

## Slide 42
Tone Response –
key points
What to look for !
Avoid
clipping – horizontal plateaus
S - shaped curves
Achieve
- Monotonic, gamma shaped curves
- Count level coverage
- RGB grouping
- Aim vs. Actual curve

## Slide 43: Targets alone are not sufficient - They need to be analyzed and used -

## Slide 44
Exposure - Difference from aim
Tolerance corridor
★★★★
★★★

## Slide 45
What causes OECFs to vary?
Non-standardized software selections
Confusing software driver settings
Individual color/tone preferences
Auto contrast selections
Lighting variability

## Slide 46: White Balance
 OECFs can be measured for each color channel
using a target’s neutral gray patches.
 85% of good color imaging performance is keeping
the Red, Green, and Blue OECFs the same… Really!
This is a good example of a well white balanced capture
Note that all color channel OECFs lie on top of each other

## Slide 47: White Balance (full scale)
This is an example where the white balance performance is marginal.
Note how the blue channel OECF departs from the red and green OECF

## Slide 48
White Balance Assessment using
Photoshop Histograms
Though gray patches appear gray, the one patch is actually slightly colored.
All three histogram should align if white balance is correct

## Slide 49
White Balance
- Keep the Neutrals neutral -
★★★★
★★★

## Slide 50
Color
Colour
Kolor

## Slide 51
Color – Its just an encoding
Same colors – different encoding
Courtesy of
L*a*b*
color
Digital
encoded
color
Input color profiles are RGB code value to real color dictionaries

## Slide 52: L*a*b*: A way to measure a single color - A 3-D space that contains all possible colors perceived by human observers - Uses color Lightness ( L*) and Hue/Saturation ( a*,b*) as parameters

## Slide 53: Color locations of a color calibration chart

## Slide 54
Δ = Difference
E = Empfindung ( sensation)
A metric for measuring human perceived
color differences, or errors, between two colors
- Uses 3 color components (L*a*b*) to measure differences.
- Several refinements (1976,1994, 2000)
- Assumes certain viewing conditions
- Meant for small differences
Measuring digital color goodness
with Delta E
(written as ΔE)

## Slide 55: How ΔE2000 is calculated for digital capture
Known L*a*b* values of
a measured color chart
RGB⌘ image of color chart
Convert average RGB values into L*a*b* values via an explicit or assumed ICC color profile
Calculate the average
RGB value for
each patch
Calculate ΔE2000 for each individual patch
⌘RGB does NOT describe color
(L*a*b*)
Present ΔE2000 statistics for all patches
Notes: Analogous to CONTROL Treatment

## Slide 56: ΔE2000 statistics for all patches

## Slide 57: Spatial Frequency Response
Foundation Metrics | Primary Metrics | Derivative Metrics
Signal | Tone Transfer Function Opto-Electronic Conversion Function (Large Area Signal ) | Tone / Exposure
 |  | White Balance
 |  | Gamma
 |  | Color / Delta E
 | Spatial Frequency Response (Small Area Signal ) | Resolution
 |  | Sharpening
 |  | Sampling Efficiency
Noise | Light Intensity Distortions | Random / White Noise
 |  | Banding / Streaking
 |  | Vignetting / Shading
 |  | Defects
 | Geometric Distortions | Chromatic Aberration
 |  | Pincushion / Barrel
 |  | Aliasing / Moire

## Slide 58
Same sampling frequency
and pixel count
Different spot size
Different resolution
Resolution example
- Hubble Space Telescope -
Before lens modification
After lens modification

## Slide 59
SFR & Resolution target features

## Slide 60
Spatial Resolution
Two factors in a digital imaging system dictate the level of spatial resolution or detail that can ultimately be captured.
  Quantity; sampling frequency ( i.e. samples per mm, inch )
    Sets the maximum capability limit that can be realistically achieved.
  Quality; effective optical quality
    Defines the level of “blur” that the imaging optics, environmental factors, hardware, and image processing impose on the captured image.
  These are necessary but insufficient components, by themselves, for capturing spatial detail. Simply improving one to reconcile deficiencies in the other will not enhance real resolution performance.

## Slide 61: Spatial Frequency Response (SFR)- The relative change in contrast of increasingly finer spatial features
Test Pattern
Increasing spatial frequency
Lens
Imaged
Test
Pattern
Imaged
Light
Distribution
SFR or ( MTF)
Increasing spatial frequency

## Slide 62: SFR & Resolution -> Quality of data (information)
Increasing lines/inch
(line width = 1/200 “)
(line width = 1/300 “)
(line width = 1/400 “)

## Slide 63: When are 5 lines clearly distinguishable ?
Quantity
Quality

## Slide 64: Calculating Sampling Efficiency
Quality (optical limit)
Adopt an accepted optical criteria for limiting resolution.
e.g. 10% SFR frequency
Quantity (digital limit)
Determine where this criteria falls relative to
the theoretical limit for digital capture
0 %
100 %
50 %
Sampling Efficiency =
Measured Optical Limit
Theoretical Digital Limit

## Slide 65: Calculating Sampling Efficiency
Sampling Efficiency =
Measured Optical Limit (200)
Theoretical Digital Limit (300)
SFR for digital print scanner
at different sampling frequencies
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
0
50
100
150
200
250
300
spatial frequency (dpi)
SFR
250 ppi
300 ppi
500 ppi
= 66%

## Slide 66
Flatbed scanner using a linear array
fast
slow
Max. measurable frequency
at 600 dpi sampling
The horizontal (slow) scan direction SFRs are lower due to the motion of the linear
array in the scanner. The duplicate edges in both directions measure the same

## Slide 67: FADGI Sampling Efficiency criteria
★★★★ : ≥ 90%
★★★ : ≥ 80%
★★ : ≥ 70%
★ : ≥ 60%

## Slide 68: SFR – Their shapes and interpretations
Limiting resolution will generally
correspond to the spatial frequency having a 0.10 modulation transfer value
Increasing spatial frequency. Finer detail
0.0
0.5
1.0
SFR response
Sharpened
Normal
Low contrast - Flare

## Slide 69
Why limiting resolution (10%) alone
fails to predict quality & why the SFR is better for doing so.

## Slide 70
SFR results- ideal curves

## Slide 71: Sharpness vs. Resolution
Sharpness
Resolution

## Slide 72: Reproduction Scale Accuracy Does Header Data match the Actual data ? Does the Requested Data match the Actual ? data ?

## Slide 73: FADGI Scale Accuracy Criteria (2017)
★★★★ : ≤ 1.0% difference
★★★ : ≤ 2.0% difference
★★ : ≤ 3.0% difference
★ : ≤ 4.0% difference

## Slide 74
- Camera shake
mirror up/down
during strobe
- Floor shake
- F-number too high
- Focal plane /platen not parallel
Bad lenses
Image processing
SFR diagnostics

## Slide 75: Noise - Light
Foundation Metrics | Primary Metrics | Derivative Metrics
Signal | Tone Transfer Function Opto-Electronic Conversion Function (Large Area Signal ) | Tone / Exposure
 |  | White Balance
 |  | Gamma
 |  | Color / Delta E
 | Spatial Frequency Response (Small Area Signal ) | Resolution
 |  | Sharpening
 |  | Sampling Efficiency
Noise | Light Intensity Distortions | Random / White Noise
 |  | Banding / Streaking
 |  | Vignetting / Shading
 |  | Defects
 | Geometric Distortions Artifacts | Chromatic Aberration
 |  | Pincushion / Barrel
 |  | Aliasing / Moire

## Slide 76: Two Forms of Random Noise
Fine-grain noise ->
high frequency fluctuations
Course-grain noise ->
low frequency fluctuations
Both of these images have the same amount of total noise

## Slide 77: One-dimensional random noise - banding and streaking -
Following contrast enhancement
• Often found on devices using linear arrays
• Contrast and equalize enhancements are
useful in detecting such noise behaviors

## Slide 78: Scanner Noise Characterization
Instead of calculating the average count value
for each neutral patch region, the standard deviation
of the count values is calculated and plotted instead

## Slide 79: A few words on image noise
• Noise values above 5 count values should be monitored closely.
• Noise values less than 0.5 may be due to clipping or aggressive noise cleaning
• High ISO speed values yield noisier images
• Sharpening tend to increase noise levels
• Noise cleaning software should be used cautiously. If applied too aggressively it will mistake object texture for random noise and remove the texture in the photographed object.

## Slide 80: Noise - Light
Foundation Metrics | Primary Metrics | Derivative Metrics
Signal | Tone Transfer Function Opto-Electronic Conversion Function (Large Area Signal ) | Tone / Exposure
 |  | White Balance
 |  | Gamma
 |  | Color / Delta E
 | Spatial Frequency Response (Small Area Signal ) | Resolution
 |  | Sharpening
 |  | Sampling Efficiency
Noise | Light Intensity Distortions | Random / White Noise
 |  | Banding / Streaking
 |  | Vignetting / Shading
 |  | Defects
 | Geometric Distortions Artifacts | Chromatic Aberration
 |  | Pincushion / Barrel
 |  | Aliasing / Moire

## Slide 81: Artifacts : Look at Images
Some imaging behavior defies objective measurement…for the time being.
  De-texturing
  Checker boarding
  Localized geometric distortions
  Sensor defects
  Color aliasing
Many are technology specific. Just knowing what type of scanner technology was used allows one to prepare for certain artifacts.

## Slide 82
Visual Inspection for Artifacts
Color Misregistration

## Slide 83
Bad Cam in a Linear array scanner
Visual Inspection for Artifacts

## Slide 84
Visual assessments of spatial artifacts is quite reliable
optical resolution limit
resolution limit due to CFA de-mosaicing
Visual Inspection for Artifacts

## Slide 85
Spatial Artifacts
Large Format Linear Array Scanner

## Slide 86
Streaking in a linear array scanner

## Slide 87
Interpolation Artifacts
4 – shot checkerboard artifact

## Slide 88
Zipper Artifacts
Crop from a good 3 star
scan, but….
Poor color interpolation

## Slide 89
So Far
Let the numbers guide
but not dictate.
Tools really do work.
But…always take a look

## Slide 90
Capability
Behavior under optimal conditions
Performance
Behavior in actual use
Don’t forget

## Slide 91
  Things vary, things go wrong
  … at transitions
  … sometimes randomly
  … mostly human and
  environmental causes
Performance Monitoring
Scan, but Verify

## Slide 92: - Performance Monitoring - OECF
Book Scanner Example

## Slide 93: Performance Monitoring – OECF four-day holiday syndrome

## Slide 95: Test plans
Test both “null” and processed ( delivered ) image files.
Explore and evaluate the image for artifacts, especially at edge transitions and on highly structured target features.
  Color misregistration
  Wavy or scalloped edges
  Near image perimeter
  moiré patterns on halftones ( view at 100%)
Have an acceptance test plan for expensive purchases.
  300, 400, 600, 800 dpi series
  On-site testing by your operators
  Evaluate over entire field of view.
  Archive test plan images for future reference and comparisons
Except for artifacts, use numbers not visual impressions as evidence.

## Slide 96
End
1907 autochrome